## Slide 1: Robotics (week 2)
Introduction to Autonomous Robots and autonomous robotics

## Slide 2: Autonomous Robotics
We will focus on autonomous robotics
Reminder - What is a robot?
  “A robot is defined as a reprogrammable, multifunctional manipulator designed to move material, parts, tools, or specialized devices through various programmed motions for the performance of a variety of tasks.” [Robot Institute of America, 1979]
  “a robot is an automatic device that performs functions normally ascribed to humans or a machine in the form of a human.” [Webster dictionary]

## Slide 3: Autonomous Robotics
What is an agent?
  In artificial intelligence, an intelligent agent (IA) is an autonomous entity which observes through sensors and acts upon an environment using actuators (i.e. it is an agent) and directs its activity towards achieving goals (i.e. it is "rational", as defined in economics) [Russel & Norvig, 2003]

## Slide 4: Autonomous Robotics
What is Autonomy?
  No remote control!
  An agent makes decisions on its own, guided by feedback from its sensors; but you write the program that tells the agent how to make its decisions environment.

## Slide 5: Our definition of a robot
Robot = autonomous embodied agent
Has a body and a brain
Exists in the physical world (rather than the virtual or simulated world).
Is a mechanical device

## Slide 6: Robot definition (cont.)
Contains sensors to perceive its own state
Contains sensors to perceive surrounding environment
Has effectors that perform actions
Has a controller that takes input from the sensors, makes intelligent decisions about actions to take, and performs these actions by sending commands to motor

## Slide 7: Robot components
All have five common components:
  Control:
    Human: Brain, central nervous system
    Function: the brain makes decisions based on sensory input , nervous system sends signals to muscles
    What is the equivalent in Robots?
      Usually the brain is a computer of some kind, wires send signals
  Effectors (body/structure):
    Human: Bones and muscles - legs, arms, wrists, neck, etc.
    Function: Allows movement
    What is the equivalent in Robots?
      Motors allow movement, wheels

## Slide 8: Robot components
All have five common components (cont.):
  Perception (sensors):
    Humans: 5 senses detected by our body (what are they?)
      Touch, Smell, Sight, Hearing, Taste
    Robots: Touch sensor notifies robot of contact with another object, sound sensor allows robot to perceive audio.
  Power source:
    Humans: food and digestive system
    Function: provide energy
    Robots: usually batteries of some kind

## Slide 9: Robot components
  Communications:
    Humans: voice, gesture, hearing
    Function: communication with outside world
    Robots: input/output functionality, expressions, wireless signals

## Slide 10: Effectors
Any device that affects the environment
  Include legs, wheels, arms, etc.
Actuator:
  The mechanism that allows the effector to execute the action
  Converts software commands into physical movements
    Through electronic or hydraulic signals
Specific categories:
  Manipulators: Industrial robot arms, capable of picking and placing objects, mimicking human
  Mobile/humanoid robots: effectors enables moving around

## Slide 11: Mobile Robots
Classified by manner of locomotion:
  Wheeled
  Legged
Stability is important
  Static stability
  Dynamic stability
https://en.wikipedia.org/wiki/Mobile_robot
https://nodna.de/H20-Wireless-Humanoid-Mobile-Robot-with-Dual-Arms_1
https://en.wikipedia.org/wiki/Roomba

## Slide 12: Industrial Robots
Robot system used for manufacturing
  Automated and programmable
  Typically stationary, include jointed arm and gripper
    Typically no legs or wheels
    Attached to a fixed surface
https://en.wikipedia.org/wiki/Industrial_robot

## Slide 13: Degrees of Freedom
Number of directions in which robot motion can be controlled
Free body in space has 6 degrees of freedom:
  Three for position (x,y,z)
  Three for orientation (roll, pitch, yaw)
https://en.wikipedia.org/wiki/Six_degrees_of_freedom

## Slide 14: Degrees of Freedom
Roll, pitch, yaw:
  Degrees of freedom used for orientation:
  Yaw refers to the direction in which the body is facing
    i.e., its orientation within the xy plane
  Roll refers to whether the body is upside-down or not
    i.e., its orientation within the yz plane
  Pitch refers to whether the body is tilted
    i.e., its orientation within the xz plane
https://en.wikipedia.org/wiki/Six_degrees_of_freedom

## Slide 15: Degrees of Freedom

## Slide 16: Degrees of Freedom
If there is an actuator for every degree of freedom, then all degrees of freedom are controllable => holonomic
Most robots are non-holonomic

## Slide 17: Sensors
Provide perception
  Proprioceptive: measure robot’s internal values
    know where you joints/sensors are
      Motor speed, wheel load, battery status
  Exteroceptive: Information from the environment
    know where you are
      Distance from objects, intensity of ambient light, etc.
Function: to convert a physical property into an electronic signal which can be interpreted by the robot in a useful way
http://www.efxkits.com/blog/various-types-of-sensors-applications/

## Slide 18: Sensors
Property sensed and sensors:
  Sound Level:
    Microphone, sound sensor
  Light:
    Camera, photo cell, light sensor
  Distance:
    Ultrasound, radar, infra-red®
  Contact:
    Bump/switch, touch sensor
  Inclination:
    Gyroscope
  Others:
    Smell sensor (chemical), temperature (thermal), altitude (altimeter)

## Slide 19: Sensors (cont.)
Operation:
  Passive: read a property of the environment
    Cameras when not using flash
      Using naturally emitted light from the sun
  Active: act on the environment and read the result
    Camera when using flash
      Illuminates its target and measures the energy reflected back

## Slide 20: Sensors (cont.)
Are sensors always accurate?
  Noise may interfere with measurements
    Internal: from inside the robot
    External: from the Robot’s environment
    Calibration: can help eliminate/reduce noise

## Slide 21: Environment
Accessible vs. inaccessile
  Does the robot have access to all the information required to make decisions?
Deterministic vs. non-deterministic
  Does any action that the robot undertakes have only one possible outcome?
Static vs. dynamic
  Does the environment changes only due to robot actions, or does it also change by itself?
Discrete vs. continuous
  Do sensors and actions have a discrete set of values?
https://www.sdl.com/about/corporate-citizenship/environment/

## Slide 22: State
Knowledge about oneself and one’s environment
Kinematics == study of correspondence between actuator mechanisms and resulting motion
  Relationship between robot dimensions, position and resulting velocity and acceleration
    Rotary or linear motion
Combines sensing and acting
  Did I go as far as I intended?
But environment is full of information
  For an agent, need to pick relevant input

## Slide 23: Why Robots?
Can perform dirty, dangerous or dull tasks
Where can we replace humans with robots?
  Home
    Roomba
  Industry
    Manipulator robot for building cars
  Medical
    Surgical robots
  War
    Bigdog (hw assignment next week)
  Other places?

## Slide 24: Homework Assignment
Read both articles about BigDog and answer the following questions:
  What is BigDog (1 pt.)
  Who is the sponsor of the BigDog project (0.5 pt)
  What is the ultimate goal of this project (0.5 pt)
  Describe the five components (controls, actuators, sensors, power source and communications) of BigDog (2 pt)
  What is BigDog currently capable of? (1 pt)

## Slide 25: Homework Assignment
Due: unit B.1
Submission format: You should submit hardcopy (typing is strongly recommended or writing clearly) before beginning of class time on the due date. If you have difficulty submitting a hard copy, email is acceptable. Assessment is not acceptable after we discuss it in class.